## Slide 1
Floating Systems Optimization Check-In
Garrett Barter
August 2, 2018

## Slide 2: FY18 Achievements
Full floating offshore wind energy representation in WISDEM (minus O&M)
  New modules: FloatingSE, OffshoreBOS
  Improvements throughout WISDEM for cohesiveness, ease of use
“Tabula rasa” (blank slate) design of floating substructure using a genetic algorithm optimizer, bounded design variables, and constraints
  No initial “feasible” point, just a randomized sampling of design space
  Mixed-integer optimization for continuous (e.g. diameter) and discrete (e.g. # mooring lines) design variables
Visualization of results

## Slide 3: Spar optimization
Spar design seems most reasonable
  Tough to get it wrong
Lots of mooring lines for reasons not yet completely understood
  Would not invalidate any substructure weight sensitivity studies
Full view
Zoom
Top view

## Slide 4: Sensitivity around optimized spar design
Have already run initial weight sensitivity study on final spar design
  Results are not yet “fully optimized”, but show a clear trend
Approximately linear 1:1 reduction in substructure mass for reduction in RNA mass

## Slide 5: Semisubmersible optimization
Most of buoyancy is coming from main column and pontoons
  Large pontoons because need stiff cross members and only have pipe-cross section available (still requires further scrutiny)
Needed improvements:
  Heave plates so that the optimizer doesn’t try to flare the columns
  Need to add some constraints so that offset columns don’t emerge from water during heel
Would argue can still run weight sensitivity study
Full view
Zoom
Zoom-ier

## Slide 6: TLP optimization
Design that is most suspect
  Too many offset columns(6)
  Draft is too deep
What we see is not yet ”fully optimized”
Would like to re-run before committing to weight sensitivity study
Full view
Zoom
Top view

## Slide 7: Next Steps
Near Term (by end of FY18)
Dive in to sensitivity more
  What is changing: Diameter / ballast / thicknesses, etc?
  Compare to Senu’s old results
  Breakeven cost analysis
Do a sensitivity for tower mass as well?
Include semisubmersible sensitivity analysis too
Write a study report detailing methodology and findings, polish FloatingSE documentation
Long Term (FY19 and beyond)
Hydrostatics-only, single DLC approach might be too low of fidelity to give credible results
A linear potential-flow, frequency-domain approach might be more credible yet still fast enough for optimization
(this improvement will be part of “Concept Paper Proposal”)